regulatory standards AND RULES ON NUCLEAR AND RADIATION SAFETY

# RADWASTE SAFETY

PROCEDURE FOR EXEMPTION OF RADIOACTIVE WASTE AND radioactive BY-MATERIALS FROM REGULATORY CONTROL

NP 306.3.04/2.002-97

## Official Edition

Ministry for Environmental Protection

and Nuclear Safety of Ukraine

KYIV

1997

introduction

- developed

“ATOMAUDIT” Ltd.

- introduced

by the Department of Radiation Technologies and Radioactive Waste of the Ministry for Environmental Protection and Nuclear Safety of Ukraine

3. approved and implemented

By Common Decree of the Ministry for Environmental Protection and Nuclear Safety and the Ministry for Health of Ukraine No.183/331 dated 17 November 1997

4. Regulatory act complies with IAEA publications Principles for the Exemption of Radiation Sources from Regulatory Control. Safety Series 89. Vienna: IAEA. 1988, Clearance Levels for Radionuclides in Solid Materials. Application of Exemption Principles. Interim Report for Comment. IAEA-TECDOC-885. Vienna: IAEA. 1996.

5. Registered

by the Ministry for Justice of Ukraine No. 583/2387 dated 10 December 1997.

6. implemented for the first time

7. developers: O. Mykolaichuk (Leader of development), G. Burlak, A. Varbanets, T. Berezhnaya, A. Sakharova

________________________

This regulatory act can not be completely or partially reproduced, replicated, and distributed as an official issue without the permission of the Ministry for Environmental Protection and Nuclear Safety of Ukraine

Contents

1 General provisions

2 Main terms, notions, and their definitions

3 Criteria for exemption of radioactive waste and radioactive by-materials from regulatory control

4 Requirements for materials substantiating exemption of radioactive waste and radioactive by-materials from regulatory control

REGULATORY STANDARD AND RYLES ON NUCLEAR AND RADIATION SAFETY

Radwaste Safety

Procedure for Exemption of Radioactive Waste and By-materials

from the Regulatory Control

__________________________________________________________________

Valid since 1998-01-01

- GENERAL PROVISIONS

1.1. The Procedure for exemption of radioactive waste and by-materials from the regulatory control (hereinafter - the Procedure) has been developed in accordance with the Law of Ukraine “On Nuclear Energy Use and Radiation Safety” and the Law of Ukraine “On Radioactive Waste Management”, and it establishes the criteria and procedure for safety assurance in the exemption of radioactive waste and by-materials from the regulatory control, and it refers to standards, rules, and regulations on radioactive waste management.

1.2. The Procedure requirements cover all activities in liquid and solid radioactive waste management generated at nuclear facilities, as well as in the use of radiation technologies in the industrial area, agriculture, medicine, and scientific research in the following cases:

- in generation (in nuclear energy use) of radioactive waste of very low specific activity with decontaminated surface contamination, which can be considered directly or after decontamination and/or buffer storage those subject to the exemption from further regulatory control;

- in introduction of radioactive waste processing technologies, which provide for discharge of individual flows of treatment products that can be disposed of or reused without applying regulatory control to them;

- in secondary use of materials containing radionuclides or contaminated by them within the nuclear-fuel cycle, or radiation technologies, including buffer material of limited use.

1.3. The exemption of radioactive waste and by-materials from the regulatory control is performed by the state regulatory authority on nuclear and radiation safety according to the authorized procedure.

1.4. The exemption of radioactive waste and by-materials from the regulatory control can be performed at any stage of their management.

1.5. The quantity of radioactive waste and by-materials exempted from the regulatory control is limited by the quantitative limit determined based on dose criteria in each specific case.

1.6. The exemption of radioactive waste and by-materials from the regulatory control can be both final and restricted.

1.7. Radioactive waste and by-materials, which can not be considered radioactive because of their low activity, are exempted finally from the regulatory control, if there is no need for determining methods for radioactive waste disposal or treatment, and introducing new restrictions.

1.8. The disposal or treatment methods should be determined, the exemption levels should be established, and the possibility of transferring radioactive waste and by-materials for another juridical person should be substantiated in case of the restricted exemption from the regulatory control.

- MAIN TERMS, NOTIONS, AND THEIR DEFINITIONS

Buffer storage – the storage of radioactive waste and radioactive by-product materials in a specially designated facility for a definite time, ensuring a decrease in radioactive waste activity through the natural decay of radionuclides.

Derivative exemption level – the value used as a criterion in measuring radiation characteristics of radioactive waste which is determined taking into account the applied methodological provision and hardware and considering the established level of the exemption.

Exemption level – the limit of activity or radioactive contamination established by the state nuclear and radiation safety regulatory authority expressed in terms of activity concentrations and/or total activities, at or below which sources of radiation can be released from nuclear regulatory control.

Final exemption from the regulatory control – the complete exemption from the regulatory control without determination of specific conditions.

Radioactive by-product materials – radioactive materials produced due to operation of nuclear facilities as well as under using of radiation technologies in industry, agriculture, medicine and researches and which can be used again.

Radioactive waste – material objects, and substances whose radionuclide activity or radioactive contamination exceed the limits established by current regulatory standards provided that the use of these objects and substances is not foreseen.

Regulatory control – control by nuclear and radiation safety regulatory authority based upon the system of notification, registration and licensing that allows the competent authority to establish appropriate safety requirements.

Restricted exemption from the regulatory control – the exemption from the regulatory control under which the state regulatory authorities determine specific conditions regarding transferring radioactive waste and by-product materials to other persons, methods for the disposal or treatment of radioactive waste and materials, limits regarding the activities, etc., and supervise over their implementation.

- CRITERIA ON EXEMPTION OF RADIOACTIVE WASTE AND BY-MATERIALS FROM REGULATORY CONTROL

3.1. Exemption from the regulatory control should not cause exceeding of the main dose limits established in regulatory standards on radiation safety in force.

3.2. Physical, chemical, and other properties of radioactive waste should be taken into account in reviewing the possibility of exemption from the regulatory control in order to prevent cases of the exemption from the regulatory control of radioactive waste whose non-radioactive properties can cause increasing radiation hazard. Inflammable and volatile radioactive waste and by-materials can not be exempted from the regulatory control.

3.3. The main dose criteria determining the possibility for exemption of radioactive waste and by-materials from the regulatory control are:

- individual equivalent dose for the critical group should not excess 0.05 (Sv per year;

- collective dose conditioned by the activity on management of radioactive waste exempted from the regulatory control should not excess 1 man-(Sv per year.

3.4. Radioactive waste and by-materials whose radioactive characteristics meet the following exemption levels (in case of unknown nuclide content of radioactive waste) are subject to final exemption:

- total specific activity averaged for a batch of radioactive waste, but not more than for 1000 kg, does not exceed 1 kBq/kg for beta- and gamma-radiation sources, or 100 Bq/kg for alpha-radiation source, and the mass of radioactive waste should not exceed 3 000 tons per year in this case;

- total activity of a single package containing less than 100 kg of radioactive waste is not more than 100 kBq for beta- and gamma-radiation sources, or 10 kBq for alpha-radiation sources;

- the following surface contamination exemption levels are established for structural materials in nuclear facilities decommissioning:

| alpha-radiation | 0.05 Bq/cm2 (exemption level is 5000 Bq) |
| --- | --- |
| beta- and gamma-radiation | 5 Bq/cm2 (exemption level is 5000 kBq) |
| other radionuclides | 0.5 Bq/cm2 (5000 Bq<exemption level<5000 kBq) |

3.5. The exemption levels under the restricted exemption from the regulatory control are established in each specific case based on calculations of individual and collective doses for the possible scenarios and ways of their formatting.

3.6. In the restricted exemption for regulatory control covering different sites, the amount of radioactive waste and by-materials exempted from the regulatory control is restricted by introducing (both in whole and for each separate site) the annual quotas regarding the volume (activity) based on probable contribution in the collective dose from radioactive waste management activities exempted from the regulatory control.

3.7. Safe management of radioactive waste and by-materials exempted restrictedly from the regulatory control is conditioned by the quality system providing the guarantee that radioactive waste meet the established criteria, and their further management is performed by the stipulated way.

3.8. Proper technological, technical, and materials conditions providing their further safe management should be created before making the decision on the restricted exemption of radioactive waste and by-materials from the regulatory control.

- REQUIREMENTS FOR MATERIALS SUBSTANTIATING EXEMPTION OF RADIOACTIVE WASTE AND BY-MATERIALS FROM REGULATORY CONTROL AND THEIR REVIEW

4.1. Radioactive waste and by-materials are exempted from regulatory control on a basis of review of the application and substantiating materials submitted by a juridical person responsible for these radioactive materials by the Nuclear Regulatory Administration of the Ministry for Environment Protection of Ukraine.

4.2. The juridical person responsible for this radioactive waste and by-materials is also responsible for substantiating the possibility of radioactive waste and by-materials exemption from the regulatory control, and derivative quantitative criteria for each specific case (exemption levels).

4.3. The following information should be provided in the application on exemption from the regulatory control:

- technological source of radioactive waste and by-materials provided for the exemption from the regulatory control, and general description of their physical, chemical, and radiation characteristics;

- further foreseen purpose of the mentioned radioactive waste (final exemption from the regulatory control, buffer storage with subsequent final exemption from the regulatory control, and secondary use with transferring to another juridical person, or without it);

- provided derivative levels of the exemption of radioactive waste and by-materials;

- provided quantity of radioactive waste and by-materials subject to the exemption from the regulatory control, which is expressed by the total activity, as well as the weight and scope.

4.4. Substantiating materials should include:

4.4.1. A license issued to the juridical person responsible for radioactive waste and by-materials reviewed.

4.4.2. Sanitary certificate (or document substituting it).

4.4.3. Feasibility study of the exemption of radioactive waste and by-materials from the regulatory control including:

- description of origin and characteristics of radioactive waste and by-materials;

- analysis of expenses and effectiveness associated with the exemption of the radioactive waste and by-materials from the regulatory control;

- methods and hardware used for determining the activity of radioactive waste and by-materials;

- method for disposal or treatment of radioactive waste and by-materials;

- evaluation of radiation impact of radioactive waste and by-materials exempted from the regulatory control on the personnel, public, and environment.

4.4.4. Quality assurance program or extracts from it specifying measures and methods ensuring that the attribution of radioactive waste and by-materials to those exempted from the regulatory control, and their management is performed in a proper way.

4.4.5. Environment impact report of the established form.

4.4.6. Positive conclusions of the State Health Sanitary Expert Review, which is performed according to legislation in force in Ukraine.

4.4.7. Positive conclusions of the State Ecological Review carried out according to the procedure established by the Law of Ukraine “On State Ecological Review”.

4.5. If the positive conclusions of obligatory reviews are available, and all corresponding requirements of regulatory standards and rules on nuclear and radiation safety are fulfilled, the Nuclear Regulatory Administration issues a permit for exemption of radioactive waste and by-materials from the regulatory control where it is necessary to indicate:

- characteristics identifying radioactive waste and by-materials exempted from the regulatory control (origin, type, and exemption levels);

- condition of exemption from regulatory control;

- term of exemption from regulatory control (under the limited exemption).

4.6. The state nuclear and radiation safety regulatory authorities verify management conditions of radioactive waste and by-materials exempted restrictedly from the regulatory control with the periodicity of at least once per year.